## Slide 1
DEFIBRILLATOR SUPPORT HUB
Is it time to replace your
school defibrillator?
Not just because a battery or pad quote is expensive.
Identify the exact model, confirm support and compatibility, then compare the whole-life cost of keeping it with replacement.
General guidance - follow the AED manufacturer's instructions for your device.
Notes: Opening: explain that this is a spending and readiness check, not a device-specific clinical recommendation.
[Sources]
Department for Education, Automated External Defibrillators (AEDs): Guidance for schools, January 2025: https://assets.publishing.service.gov.uk/media/67936b102de28ea2d392f35b/Automated_External_Defibrillators__AEDs__guidance_for_schools.pdf
First Aid Garage approved retained brand artwork: Paul and Janette character asset and circular logo.

## Slide 2
FIRST AID GARAGE
CHECK THE DEVICE FIRST
Four facts decide the next step
Take a clear photo of the model label before contacting any supplier.
1
Exact identity
Make, model, serial number and compatible part number
2
Readiness
Pad/battery expiry dates and ready or fault indicator
3
Support
Manufacturer support, software updates and parts availability
4
Remaining life
Documented anticipated service life - not warranty alone
Compare replacement when...
✓
Correct consumables are no longer available.
✓
The model is unsupported or discontinued.
✓
It is at or beyond its anticipated service life.
A high consumable cost for a very old device is a reason to compare - not an automatic instruction to replace.
Never order pads or a battery by appearance alone. Confirm exact model compatibility.
Training today, saving lives tomorrow. | General guidance
2
Notes: Use the four facts to stop staff comparing headline prices without understanding compatibility or remaining service life.
[Sources]
DfE guidance, pages 33-34: correct consumables are not usually interchangeable; follow manufacturer replacement periods; anticipated service life differs from warranty; replacement is needed when pads and batteries cease to be available.
https://assets.publishing.service.gov.uk/media/67936b102de28ea2d392f35b/Automated_External_Defibrillators__AEDs__guidance_for_schools.pdf

## Slide 3
FIRST AID GARAGE
BEFORE YOU SPEND
Compare the whole-life cost, not the box price
Ask the supplier to put these details in writing.
What exactly are we buying?
✓
Exact make and model
✓
Included pads, battery, case, sign and prep kit
✓
Adult and paediatric capability
✓
Warranty, anticipated service life and support
✓
Pad/battery costs and replacement intervals
Use trusted checks
DfE guidance
Printed page 15 explains the reduced-cost arrangement. Get today's price from the scheme/supplier and compare Appendix A's minimum specification.
BHF pads & batteries
Useful for supported, identifiable devices only. It cannot guarantee a part for every discontinued AED.
The Circuit
Keep location, access, pad expiry and emergency-ready status current.
Current prices change: do not quote an old fixed figure.
Training today, saving lives tomorrow. | General guidance
3
Notes: Close by agreeing who will photograph the label, check readiness, contact technical support and keep The Circuit record current.
[Sources]
DfE purchasing section, printed page 15 / PDF index 14, and Appendix A minimum specification: https://assets.publishing.service.gov.uk/media/67936b102de28ea2d392f35b/Automated_External_Defibrillators__AEDs__guidance_for_schools.pdf
British Heart Foundation pads and batteries shop: https://defibrillators.bhf.org.uk/pads-and-batteries
The Circuit national defibrillator network: https://www.thecircuit.uk/